## Slide 1: Inspire Product Redesign
Landon Willey

## Slide 2: Problem Statement
Kitchen Shelving Unit
About 2 ft x 1 ft x 2.5 ft
Three Shelves
Minimize weight for current application (<30 lbs per shelf)

## Slide 3: Inspire Tools
Geometry
  Cut: Separated the design space from the rest of the model
  Push/Pull: Created areas where the loads can act (since the loads can’t act directly on the design space)
Structure
  Supports: Modeled the base of each leg as a pin support
  Loads: Simulated objects as point loads on solid plates on each shelf
  Gravity: Simulated the weight of the structure
  Symmetry: Constrained the shelf shape to be symmetric (excluding the x-y plane)

## Slide 4: Results
Minimize mass with a safety factor of 2.0 was unable to produce a structure
Minimize stiffness resulted in an undesirable structure
Mass was reduced from 88.7 lbs to 34.5 lbs, a 60% reduction

## Slide 5: Discussion
The inability to produce a structure was a common problem with the optimization of other objects as well
  Three total objects were attempted (robot base and two different styles of shelves)
  In each case, the program prompted to use more realistic loads, but gave no further information as to why the structure couldn’t be optimized
The minimum member size combined with runtime was a major limiting factor of the program
  The actual shelf had 1/16 in. diameter members
  Inspire was unable to optimize with minimum members greater than 1/3 in.
  Smallest minimum member size with <30 minute runtime was 1 in.
The shape determined was not innovative
  While many of the truss structures were unique and interesting, the design for the shelf was essentially a thinner shelf
  The actual wire-frame construction was more unique than Inspire’s result

## Slide 6: Conclusion
Inspire was not able to create a desirable design with the parameters given and the resources allocated
For this type of an analysis, a more advanced knowledge of how to set up a design in Inspire would be required